## Slide 1: LundaLoggern
Smart Data Logging for Intensive Care Ventilators
Åke | 2026-03-16

## Slide 2: The Problem
Intensive care ventilators generate critical patient data — but capturing it consistently is hard
  Long term data logging in SERVO very limited.
  The Getinge Servo-logger requires a PC bedside
Manual data recording is error-prone and time-consuming for clinical staff
Existing solutions are often expensive, complex, or tied to proprietary hospital IT systems
How can we make ventilator data logging simple, portable, and independent?
Why ventilator data capture needs to be easier

## Slide 3: Introducing LundaLoggern
A plug-and-play data logger for SERVO ventilators
Small, self-contained device — no hospital network or IT integration needed
Connects directly to the ventilator’s CIE port
Automatically records breath-by-breath data, settings, and waveforms to SD card
Built-in colour display shows live status at a glance
Built-in WiFi lets you download data from your phone or laptop

## Slide 4: How It Works
Step 1 — Plug in
  Connect LundaLoggern to the ventilator’s CIE port
  Data collection configuration can be made off-line
Step 2 — Auto-detect
  The device identifies the ventilator and starts logging immediately
Step 3 — Enable WiFi
  Press the button and scan the QR code on the display
Step 4 — Download
  Open the web dashboard on your phone or laptop to review and download data files
Four simple steps — no training required

## Slide 5: What Gets Logged
Comprehensive, configurable data capture
Breath metrics
  Tidal volume, respiratory rate, minute ventilation, FiO₂, PEEP, peak pressure, and more
Ventilator settings
  Mode, patient category, compliance compensation, I:E ratio
Waveforms
  Flow, airway pressure, volume, CO₂, Edi — fully configurable
All data timestamped automatically using the ventilator’s own clock
Choose which parameters to track via simple text files on the SD card

## Slide 6: Key Features & Benefits
Designed for simplicity, privacy, and portability
Plug-and-play
  No setup, training, or IT support needed
WiFi off by default
  Minimises RF interference in the ICU
  Connection possible only when requested
Portable & compact
  Fits in a pocket; move between ventilators
SD card storage
  Standard, removable, unlimited capacity
QR code connectivity
  Connect to WiFi in seconds
Configurable logging
  Adapt to research or clinical needs
Live display
  Connection status, ventilator ID, timestamps
No cloud dependency
  Data stays local — patient privacy ensured

## Slide 7: Target Markets & Use Cases
Clinical / Neonatal ICU
  Continuous monitoring for quality assurance
  Research data collection during clinical studies
Biomedical Engineering
  Performance verification and troubleshooting
  Long-term trend analysis during service calls
Medical Device R&D
  Bench testing and field validation of prototypes
  Rapid data capture without proprietary software
Education & Training
  Teaching tool for respiratory therapy programs
  Live data demonstration during training sessions

## Slide 8: Competitive Advantages
No recurring costs
  No licenses, subscriptions, or cloud fees
Vendor-independent data
  Plain text files — open and portable
No hospital IT involvement
  Standalone device with its own WiFi access point
Privacy by design
  Data never leaves the device unless the user downloads it
Low-cost hardware
  Built on the widely available ESP32-S3 platform
Fast deployment
  Working in under a minute, zero configuration required
Why LundaLoggern stands out

## Slide 9: Product Demo
What you see on the device and on your phone
TFT display shows:
  Ventilator type and serial number
  SD card and COM status indicators
  WiFi IP address and QR code
Web dashboard on any device:
  File listing with timestamps
  One-tap download and delete
  Configuration viewer
SERVO Log Viewer
  Device independent data viewer

## Slide 10: Technical Snapshot
Hardware
  LilyGo T-Display S3 (ESP32-S3), SD card reader, RS232 interface
Display
  320 × 170 px colour TFT
Connectivity
  WiFi access point — no internet needed
Protocol
  SERVO CIE interface (standard on all SERVO ventilators)
Power
  USB-C — can be powered from the ventilator’s USB port
  Uses power only USB cable, i.e. no communication to ventilator Panel
Software
  Open-source Arduino / PlatformIO firmware
Quick reference — key specs at a glance

## Slide 11: Roadmap
Future possibilities
WiFi auto-shutoff after 5 minutes of inactivity
Bluetooth connectivity for direct mobile app integration
Multi-ventilator support — expand beyond SERVO to other brands
Cloud sync option (opt-in) for centralized research data collection
Real-time trend graphs on the web dashboard
Battery operation for transport and ambulance use
Regulatory pathway — CE marking / FDA clearance for clinical deployment

## Slide 12: Call to Action
What we need from marketing:
  Market sizing and customer segmentation feedback
  Input on branding, naming, and visual identity
  Channel strategy — direct sales, distributors, OEM partnerships?
  Pricing model validation
“We have a working prototype — let’s bring it to market.”

## Slide 13: Q & A
Thank you!

## Slide 15: LundaLoggern

## Slide 16: LundaLoggern